## Slide 1
DNP @ UNH: Vector and Tensor Polarization Extraction from Line-Shape Analysis
Michael McClellan
Department of Physics, University of New Hampshire, Durham, NH 03824

## Slide 2
Background
Solid Polarized Target Group at UNH
  developing dynamically polarized target
  measure spin-structure & tensor spin observables
    AZZ, T20 and b1
E. Long et al., C-12-15-005 PAC 44 (2016)

## Slide 3
Proton Signals
Spin polarized protons: low T, high B → energy gap between spin states → uneven distribution
  Thermal equilibrium (TE) signal – can be enhanced
  Detectable through nuclear magnetic resonance (NMR)
  Area under curve → % vector polarization (PZ)
One of our first signals!

## Slide 4
Deuteron Signals
Deuteron signal (with quadrupole splitting) more complex:
  One curve for -1 → 0, another for 0 → +1 – sum gives PZ, difference gives PZZ
  Curves span quadrupole angle distrubtion, 0-90° (up to 180° doubles back)
Ideally, NMR signal would be compared to TE signal and scaled
  TE integral is physical quantity dictated by B, T
  At 5T & 1K: PZ for deuteron ~ 0.08% - on level of noise for our lab

## Slide 5
Simulating Spin Flips
Macro that directly simulates spin flips for a given polarization
Can use to explore new avenues for increasing PZZ
Plots from code by Elena Long, drawing on: M. H. Cohen et al., Solid State Physics 5, 321 (1957)

## Slide 6
NMR Analysis
Without reliable TE, curve fit NMR lineshape to known formula from Dulya, et al.
At high PZ, physical parameters can be extracted – B, T not required!
With parameters, curve fit for r across timespan for data taking
  Naively, ratio of peak heights of signal
  Instead of area method, r is used for ratio method to find both PZ and PZZ
In materials with different bonds to deuterium (e.g. butanol – C and O bonds), set of curves for each bond type
C. Dulya et al., Nuclear Instruments and Methods in Physics Research A 398 (1997)

## Slide 7
NMR Analysis
C. Dulya et al., Nuclear Instruments and Methods in Physics Research A 398 (1997)
F-1
F+1
χ’’

## Slide 8
Data Analysis
Passing deuteron signal data through curve fitting routine based on Dulya yields good fit
  Component spin-flip curves can be reconstructed from curve fitting parameters
  Can perform both area and ratio methods!
Passing simulated data through routine extracts PZ that agrees with input!
PRELIMINARY
  PZ = 28.2%
  PZZ = 6.1%

## Slide 9
Real & Imaginary Analysis
Issue with Dulya – “false asymmetry” – seems artificial – why not just fit both real and imaginary parts of signal?
Two different parts to signal – absorptive and dispersive – rotate between through phase angle
  Real = χ’’ cosθ - χ’ sinθ
  Imag. = χ’’ sinθ + χ’ cosθ
Changes for dispersive:
PRELIMINARY

## Slide 10
Real & Imaginary Analysis
Preliminary agreement between PZ and PZZ taken from real and imaginary signals!
VERY PRELIMINARY

## Slide 11
Increasing PZZ
Increasing PZ via mm-wave enhancement naturally gives PZZ
  Signal skews as it gets bigger
To increase further, can use hole-burning: separate solenoid fires at specific frequency to drive spin flips – increase area difference
  Lose some PZ but for AZZ, PZZ is more important
Other options:
  Rotating target cup
  Solid crystal of ND3
PRELIMINARY

## Slide 12
Future Goals
Reach PZZ of ~30% in deuterated ammonia
  Continue with hole-burning
  Use EPR to focus mm-wave frequencies
Add hole-burning to curve-fitting method – in progress!
Continue simulations:
  Can component spin-flip signals be separated in frequency?
  Reduce signal width by manipulating quadrupole angles in material

## Slide 13
Acknowledgments
UNH DNP PIs:
  Elena Long
  Nathaly Santiesteban
  Karl Slifer
UNH DNP collaborators:
  Anchit Arora
  David Ruth
  Zoe Wolters
  Allison Zec
This work is supported by the Dept. of Energy Grant DE-FG02-88ER40410.

## Slide 14
Deuteron-Electron Energy Levels