## Slide 1: Improving Qubit Readout with Autoencoders
Piero Luchi 8 September 2023
Quantum Science and Technology in Trento
ECT* workshop:
Many Body Quantum Physics and Machine Learning

## Slide 2: Outline
Dispersive qubit readout for superconducting qubits
Standard readout models
Improving qubit readout with autoencoders

## Slide 3: Qubit – Cavity system
Qubit - readout cavity system described by Jaynes-Cumming model:

## Slide 4: Dispersive Regime
Dispersive Readout approach
Write the equation in the dispersive regime
Dispersive approximation

## Slide 5: Dispersive Qubit Readout
Dispersive shift of the resonator frequency based on the state of the qubit
Measurement: Indirectly measuring the qubit state by measuring the resonator frequency shift.

## Slide 6: Dispersive Qubit Readout
Input signal
Full Demodulation
signal
I
Q
Output signal
Signal manipulation

## Slide 7: Results of Readout
According to the qubit state, the point will fall in different part of the I-Q plane.
Labelled data: Prepared in state 0 (or 1) and immediately measured.

## Slide 8: Qubit Readout: Classification
How to assign the correct label to each point?
?
Unlabelled data
Labelled data

## Slide 9: Qubit Readout: Classification
How to assign the correct label to each point?
Dataset:
  Prepare many times each state and measure it immediately
Methods :
  Gaussian Mixture models
  Neural Networks
  Neural Network with Autoencoder-type Pre-training

## Slide 10: Readout Classification: 1. Gaussian Mixture Model (GMM)
Sharp edge
Optimize parameters of a superposition of Gaussians
Real data
GMM labelled data
Problems:
Incorrect classification of many points
Not good for long or short measurements

## Slide 11: Qubit Readout: Demodulation
Full Demodulation
signal
I
Q
Sliced Demodulation
Time average
Input signal
Output signal
Signal manipulation
Turn to a finer-grained signal

## Slide 12: Readout Classification: 2. Feed-Forward Neural Network (FFNN)
Lienhard, Benjamin, et al. "Deep-Neural-Network Discrimination of Multiplexed Superconducting-Qubit States." Physical Review Applied 17.1 (2022): 014024.
Try to use all information available

## Slide 13: Readout Classification: Feed-Forward Neural Network (FFNN)
FFNN labelled data
Labelled (real) data
13
gradual transition
Problems:
Lower performance for long measurements

## Slide 14: Readout Classification: 3. Autoencoder-type Pre-training Neural Network (PreTraNN)
An autoencoder an artificial neural network that learn a compressed representation of input data by encoding it into a lower-dimensional space and then decoding it back into its original form.
It minimizes the reconstruction error.
Feature extraction, dimensionality reduction
Pre-training of feed-forward neural network
Unsupervised approach
14
Encoded/synthetic representation
encoder
decoder
Input
Input

## Slide 15: Readout Classification: 3. Autoencoder-type Pre-training Neural Network (PreTraNN)
are noisy, difficult to discriminate.
h should retain only the important features of the readout signals
Inner dimension should be optimized.
We train the autoencoder on readout data
We obtain a low dimensional representation h of readout signals
Encoded representation

## Slide 16: Qubit Readout: 3. Autoencoder-type Pre-training Neural Network
Train the new neural network on the encoded representation h of the readout signals, rather than on the readout signal itself.
This should improve the classification accuracy.
16
Neural network
LP et al. Phys. Rev. Applied 20, 014045 (2023)

## Slide 17: Qubit Readout: 3. Autoencoder-type Pre-training Neural Network
Putting it all together...
17
Encoder
Neural network
LP et al. Phys. Rev. Applied 20, 014045 (2023)

## Slide 18: Qubit Readout: Summary
Gaussian Mixture
Neural Networks
PreTraNN

## Slide 19: Classification accuracy: Measurement duration
Wide range of measurement times.
Autoencoder method (PreTraNN) has a better classification accuracy.

## Slide 20: Classification accuracy: Distributions
Neural network-based methods produce more realistic distributions.
20
GMM
exact
74,4
PreTraNN
Readout 8000 ns

## Slide 21: Conclusions
Dispersive readout in superconducting qubits
Common techniques to classify readout data
Autoecoder-based model to improve the classification accuracy